## Slide 1: Exploiting Asymmetric Systems with Flexible System Software
Barcelona, 12 July 2016
Kallia Chronaki
Thesis advisors: Rosa M. Badia and Eduard Ayguade
Research Plan

## Slide 2: The HPC Challenge
High performance computers are very power hungry!
The main challenge nowadays is to design energy efficient supercomputers
The MontBlanc project:
  Use of mobile processors to build a supercomputer!
  Mobile processors are designed to operate on low power yet offer high performance
This thesis:
  Focus on the use of asymmetric multi-core systems for HPC

## Slide 3: Asymmetric Multi-Core Systems
A new type of Heterogeneous multi-core system
Different types of cores that share the same instruction set architecture (Single-ISA)
Cores are designed with different performance or energy optimization points
  One type of cores might target performance
  Another type of cores might target energy efficiency
Our Platform for this thesis: ARM big.LITTLE
  Four out-of-order (big) cores
    Designed for performance
  Four in-order (little) cores
    Designed to operate on low power
Using such systems in HPC is not trivial

## Slide 4: Moving from Symmetric to Asymmetric
Load imbalance! 
Need of new schedulers and runtime systems
time
time

## Slide 5: Thesis Objectives
Analysis of Existing Approaches
Task Scheduling
Runtime Thread Migration
Asymmetry-Aware Runtime System

## Slide 6: Phase 1: Analysis of Existing Approaches
Experimenting with existing approaches
Evaluation of real scientific applications (PARSEC) using different scheduling approaches:
  Application-based scheduling
    Static Threading – done by the programmer in the application code
  System Aware OS (thread)-based scheduling
    Global Task Scheduler (GTS) [1]
    Threads move to the appropriate core depending on their workload
  Task-based scheduling (runtime)
    OmpSs programming model
    Asymmetry-unaware
[1] H. Chung et.al, “Heterogeneous Multi-Processing Solution of Exynos 5 Octa with ARM big.LITTLE Technology,” Samsung Electronics Co., Ltd., Tech. Rep., 2013

## Slide 7: Phase 1: Analysis of Existing Approaches - High-level results
The task-based approach provides the highest performance with decent energy consumption
Task-based approach minimizes EDP (energy-delay product)
Chart: Avg EDP
| 4 | 5 | 6 | 7 | 8
Static threading | 0.74432 | 1.184 | 0.89536 | 0.74329 | 0.63567
GTS | 0.75395 | 1.0237 | 0.78979 | 0.74845 | 0.65862
Task-based | 0.8009 | 0.90679 | 0.75337 | 0.66008 | 0.57584
Chart: Avg speedup
| 4 | 5 | 6 | 7 | 8
Static threading | 9.4604 | 6.8821 | 7.4649 | 8.318 | 8.5688
GTS | 9.4849 | 7.7586 | 8.7922 | 9.3345 | 9.959
Task-based | 9.2009 | 9.461 | 9.8962 | 10.5129 | 10.8726
Chart: 
| 5 | 6 | 7 | 8 | 5 | 6 | 7 | 8 | 5 | 6 | 7 | 8
Application-based
OS-based
Task-based
Number of cores
Number of cores

## Slide 8: Phase 2: Task Scheduling
We provide the knowledge of the platform to the runtime system
According to this the runtime schedules tasks to the appropriate cores (fast or slow)
Asymmetry-aware schedulers:
  Critical tasks  Fast cores
  Non-critical tasks  Slow cores
  These schedulers are:
    CATS [2]
    CPATH
    HYBRID
[2] K. Chronaki et.al Criticality-Aware Dynamic Task Scheduling for Heterogeneous Architectures in ICS’15

## Slide 9: Phase 2: Task Scheduling – High-level results on 8 cores
Chart: Speedup over little
| Cholesky 8x8 | Cholesky 16x16 | QR | Heat | Histogram | Bodytrack
BF | 7.5662 | 11.3707 | 17.2227 | 14.3189 | 6.3961 | 15.7935
dHEFT | 11.0455 | 12.193 | 19.1304 | 15.8662 | 7.7784 | 14.3948
CATS | 10.479 | 12.1286 | 19.7118 | 15.9283 | 8.3216 | 18.229
CPATH | 8.6544 | 11.2445 | 19.6018 | 11.4547 | 7.6671 | 18.0602
HYBRID | 10.2138 | 12.2077 | 20.1621 | 15.8696 | 8.1327 | 18.1442
SCHED | MIN | MAX | AVG
CATS | 6% | 38% | 19%
CPATH | -20% (HEAT) | 27%(HIST) | 6%
HYBRID | 7% | 34% | 18%
dHEFT | -10% (BODYTR) | 45%(CHOL8x8) | 14%

## Slide 10: Phase 3: Runtime Thread Migration
A different approach to provide energy efficiency
Devote one thread for the runtime activity
  Runtime activity is: Scheduling, dependence analysis
During runtime choose the appropriate type of core for this thread to migrate
  Should the runtime execute on a fast or a slow core?
  Either boosts or delays runtime
  Implement different policies for this dynamic migration
  Considering: number of tasks, dependencies, task size etc.

## Slide 11: Phase 4: Asymmetry-Aware Runtime System
Scheduling policies
  CATS
  CPATH
  HYBRID
Runtime Thread Migration Mechanisms (RTMM)
Combine the above to find the best match
  Connect each combination with the application characteristics

## Slide 12: Roadmap
Current Month
PhD Enrolment

## Slide 13: Conclusions and Expectations
The results of Phase 1 showed that the task-based approach achieves the lowest EDP
The asymmetry-aware scheduling policies (Phase 2) showed their potential in performance (up to 38% improvement)
We expect that the Runtime Thread Migration (Phase 3) will increase energy efficiency
The Asymmetry-Aware runtime system (Phase 4) is expected to overcome all existing approaches in asymmetric systems
  It is aimed to offer full utilization of the system keeping the energy consumption the lowest possible

## Slide 14: Thank you!
For further information please contact
Kallia.chronaki@bsc.es

## Slide 15: Conclusions
Our expected contributions per chapter
Task | Publication | Status
Analysis of Existing Approaches | 1 conference paper | Under review (est: 10/2016)
Task Scheduling | 1 conference paper | Accepted
 | 1 journal paper | Under review (est: 4/2017)
Runtime Thread Migration Mechanisms | 1 conference paper | TODO (est: 12/2017)
Asymmetry-Aware runtime system | 1 conference paper | TODO (est: 12/2018)